## Slide 1
Real Robot Implementation

## Slide 2
Embedded Layer

## Slide 3
ESP32
MPU9250
Magnetic Encoders
Cytron MDD10A Driver

## Slide 4
ESP32
  Why ESP32?
  After searching we saw that we can’t depend totally on Raspberry pi through all tasks. Because that’s design principle has many problem:

## Slide 5
Complexity of accessing bare metal layer at Raspberry pi
Leakage of components libraries for Raspberry pi exactly those which in C++
Power Feedback mistakes which could may damage Raspberry in just a seconds

## Slide 6
Positivity of using ESP32 rather than another MCUs

## Slide 7
ESP32 is one of oldest MCU’s which has board manager at arduino IDE, that would provide us with many resources, libraries and community sup portMPU9250

## Slide 8
ESP32 is high performance because of it’s multi-core and low cost. So it’s reliable at variety of task especially those which in Real-time and No fear of damaging it while learning of wrong wiring because of its low cost

## Slide 9
2. MPU9250
  What is MPU9250?
  MPU9250 is a combination of 3 sensors:
  Accelerometer
  Gyroscope
  Magnetometer

## Slide 10
  Accelerometer
  It used for measuring acceleration on linear axis

## Slide 11
  It Uses micro electro-mechanical systems to measure linear acceleration

## Slide 12
  This MEM looks like comp with two faces and all its teeth surrounded by left teeth and right teeth and this comp has 4 swinging ends

## Slide 13
  And as we know and the comp teeth generate capacitance when the comps swing to right (d) left get bigger and (C) left smaller

## Slide 14
  when the comps swing to left (d) right get bigger and (C) right smaller

## Slide 15
  From this measures we can exactly measure the linear acceleration.

## Slide 16
  Gyroscope:
  Gyro is used for measuring angular speed

## Slide 17
  It also depends on MEMS. But now it use Coriolis acceleration. And Newton second’s law.

## Slide 18
  Coriolis assumed that a magnetic particle with known math rotates around core and its trajectory looks like circle

## Slide 19
  If this particle rotate with constant tangential velocity. And its distance away far of core increased. And it tried to keep its tangential velocity

## Slide 20
  Its acceleration to save its tangential velocity could be calculated by

## Slide 21
  And from newton’s 2nd law , then

## Slide 22
  Magnetometer:
  Its working principle is hall effect which can be used at measuring magnetic field strength and it would be very helpful at robot localization

## Slide 23
  Finally, If we need to represent the output data of 9 DOF mpu it would be like the following:

## Slide 24
  3. Magnetic Encoders:
  It simply based on 2 hall effect sensors.

## Slide 25
  There is a core filled of magnetic slots when it starts of rotating because of attachment to motor rotor the hall effect sensor send pulses

## Slide 26
  And according of known number of magnetic slices and counting hall effect pulses we can determine exactly how much the wheel rotated.

## Slide 27
  What about finding direction?
  Easily because the existence of 2 hall effect sensors if the right-hand side pulsed first the motor would be rotate CW and if the left-hand side pulsed first then it has to be rotating CCW

## Slide 28
  And because of installing the 2 hall effect sensor with specific angular displacement. Always the first pulsed channel precede the second channel with half step

## Slide 29
  So the output at CCW
  would be like:
A
B

## Slide 30
  So the output at CW
  would be like:
A
B

## Slide 31
  And this phase shift can make me a big favor at my measures because it provide me with for different states. Which can rising my resolution 4 times up
A
B
A
HIGH
HIGH
LOW
LOW
B
LOW
HIGH
HIGH
LOW

## Slide 32
  What we need from encoder and how we get it?
  We need from encoder to supply us with angular velocity for each wheel which would be very useful for tracking our robot location.

## Slide 33
  Gratefully that we live in 21st century. Because we have a revolutionary MCUs which can easily provide us with digital inputs read the pulses of hall effect sensor pulses. And we can give this pins the priority to read these input signals using interrupts with every rise-up or fall-down for both cannels

## Slide 34
  Let’s make a sprint at mathematics.
  : pulses per revolute
  (according to our encoder)
  : 2 (channel A, B)
  according to our motor
  so we can easily know that our encoders
  = 742

## Slide 35
  2. Using MCU timer
  3. And
  4. And using timers too, we count pulses summation

## Slide 36
  5. Then we reset timers for and
  6. Count (rpm)

## Slide 37
  4. Cytron MDD10A (motor driver)
  We get to our last component,
  the motor driver. Simply, the motor driver work as gate to voltage to control motor speed. As it known for us that controlling speed using MCU need to PWM signal. And we also know that MCU maximum output is 5V.

## Slide 38
  So, this motor driver works on amplifying this PWM signal to the need voltage for our motor specs. Also, it allows us to control this PWM signal pi-directional to have the ability to rotate CCW or CW

## Slide 39
  Robotics breaking ice

## Slide 40
  First thing we had to know is Translation Form.
AMR position can be defined with a matrix as following:

## Slide 41
And now we can say that it pose at:

## Slide 42
for simplification we can say that location because the other DOFs will never be used because AMR moves at 2d plane.

## Slide 43
If AMR moved as it seen. Its pose would be (4, 5, )

## Slide 44
What if there is an obstacle front of AMR?

## Slide 45
So the translation form of obstacle would be the summation of translation form from origin to robot and from robot to obstacle

## Slide 47
If we move the robot, we send it matrix of speeds : (7, 2, 90)

## Slide 48
How our speed matrix message would act (7, 2, 90):
1. Convert linear velocity of x
from m/s to m/min
2. Convert angular velocity of z
from rad/s to rad/min
3. Calculate tangential velocity
Which : the distance between center of right wheel to left wheel

## Slide 49
4. Get angular component of
5. Get angular component of
6. Calculate wheels speeds

## Slide 50
5. Odometery
Odemetery is our AMR backbone, simply it is the updatable feedback of TF which is initially, basic & needed sensing for robot to know where is it and how much walked away of origin.

## Slide 51
The odometery has several types:
Wheel feedback
Inertial odometery
Visual odometery
Laser odometery

## Slide 52
Wheel odometery
From velocity which encoders supply us with we calculate the position matrix
convert revolutions per minute to revolutions per second

## Slide 53
Wheel odometery
From velocity which encoders supply us with we calculate the position matrix
convert revolutions per minute to revolutions per second
which : the distance between the front wheel center and rear wheel center

## Slide 54
Wheel odometery
From velocity which encoders supply us with we calculate the position matrix
convert revolutions per minute to revolutions per second
which : the distance between the front wheel center and rear wheel center

## Slide 55
Kalmn Filter
After getting this initial odometery we found that it isn’t enough simply because if the wheels move on unlevel land this odom will be usless. so., we saw that we had to depend on different sources for odom which are IMU & encoders

## Slide 56
Kalmn Filter
Kalmn filter is based on bayes rule:

## Slide 57
Kalmn Filter
Using Kalmn filter we could improve our odometery feedback response

## Slide 58
THANK'S FOR LISTENING
LARANA, INC.